## Slide 1
The Avengers of Innovation
Empowering Girls in IoT and 5G Universe
SMAP Labu, Negeri Sembilan
3 August 2024 (Saturday)

## Slide 2
IoT and 5G
(Get your hands dirty)

## Slide 3
IoT and 5G
(using Tinkercad & ESP8266)

## Slide 6
ESP 8266

## Slide 7
Task 1: LEDs Blinking
Description:
Two LEDs will be blinking alternately in sequence.
Steps:
Connect two LEDs to pin D7 and pin D8.
Write down the algorithm to perform this operation.
Mission: To turn two LEDs (pin D7 and D8) alternately ON and OFF with a period of 1 second

## Slide 8
Task 1: LEDs Blinking

## Slide 11: Task 2: Knight Rider LEDs
Mission: You are given four (4) LEDs. Turn ON and OFF each LED with 0.2s delay with knight rider pattern as shown below.

## Slide 12: Task 2: Knight Rider LEDs

## Slide 14
How can we bring this project
to life in the real world?

## Slide 15: Introduction to Arduino: Hardware

## Slide 16
Arduino UNO
ESP 8266

## Slide 17
ESP 8266

## Slide 18: ESP8266
ESP8266 microcontroller integrated with Wi-Fi and Bluetooth module.
Very practical for IoT project
  Low-cost
  Low-power
  Many GPIO pin

## Slide 19
How can we bring this project
to life in the real world?

## Slide 20: From Software Prototype (Tinkercad) To Hardware Protoype (ESP8266)
Test your design and idea in Tinkercad
Put your hardware components together (ESP, LEDs etc)
Use Arduino IDE to load the program into ESP8266

## Slide 21: From Software Prototype (Tinkercad) To Hardware Protoype (ESP8266)
Test your design and idea in Tinkercad
  Circuit connections (Arduino, breadboard, LEDs and wires)
  Write program (block-based)
  Simulate and test the program (working as expected)
  Convert the program to C++
Put your hardware components together (ESP, LEDs etc)
Use Arduino IDE to load the program into ESP8266
  Copy and paste the program to Arduino IDE
  Upload the program to ESP8266
  Verify and test your hardware (working as expected)

## Slide 22
Assemble your hardware components (ESP, LEDs etc)

## Slide 23
Connected !
Notes: About Breadboard (internal connections)

## Slide 24: From Software Prototype (Tinkercad) To Hardware Protoype (ESP8266)
Test your design and idea in Tinkercad
  Circuit connections (Arduino, breadboard, LEDs and wires)
  Write program (block-based)
  Simulate and test the program (working as expected)
  Convert the program to C++
Put your hardware components together (ESP, LEDs etc)
Use Arduino IDE to load the program into ESP8266
  Copy and paste the program to Arduino IDE
  Upload the program to ESP8266
  Verify and test your hardware (working as expected)

## Slide 25: Copy C++ Code from Tinkercad,

## Slide 26: Copy C++ Code from Tinkercad, and then Paste C++ Code in Arduino IDE

## Slide 27: Select Board

## Slide 28: Select Board and Port (it is okay if different port)

## Slide 29: Click ”Upload”

## Slide 30: Task 3: Ultrasonic Sensor Reading
Description:
The ultrasonic sensor reading will change according to the distance of object in front.
Steps:
Connect the ultrasonic sensor to the Arduino.
  Vcc to 5V
  Trig to pin D7
  Echo to pin D8
  GND to GND
Connect RED LED to pin D4
Connect RED GREEN to pin D2
Write down the algorithm to perform this operation.
Mission: Read the distance reading from ultrasonic sensor, and to the following:
Turn ON GEEEN LED if the distance less than 10 cm,
Turn ON RED LED if the distance is more than 10 cm

## Slide 32: Task 3: Ultrasonic Sensor Reading

## Slide 33
How can we bring this project
to life in the real world?

## Slide 34
Now, build your
(ultrasonic) hardware prototype

## Slide 35
IoT and 5G
(using Node-RED)

## Slide 37
Concept of IoT
Sensors
(Temperature, Humidity and Light intensity)

## Slide 38: XDK 110

## Slide 39: Dashboard

## Slide 40: Sensor, Network and Dashboard
Thing: measures and sends data
Network: provides connectivity
IOT Platform (Dashboard):
user interface for visualization
Internet
1
2
3

## Slide 43: IoT – Node-RED
Node-RED is a programming tool for wiring together hardware devices, APIs and online services in new and interesting ways.
It provides a browser-based editor that makes it easy to wire together flows using the wide range of nodes in the palette that can be deployed to its runtime in a single-click.

## Slide 44: IoT – Node-RED
Nodes
Debug
Deploy
Canvas

## Slide 45: IoT – Node-RED
Press Win key and type “cmd”
Open Command Prompt
Type “node-red”
Press Enter

## Slide 46: IoT – Node-RED
Copy the URL
Open browser and paste the URL
Press Enter

## Slide 47: IoT – Node-RED
Press the triple line
Click manage palette
Click install
Type dashboard and install

## Slide 48: IoT – Node-RED
Type worldmap
Install
Click Close

## Slide 49: IoT – Node-RED
Type moment
Install
Click Close

## Slide 50
Task #1
Hello World!

## Slide 52: IoT – Node-RED
First Activity
  Drag and place the inject node inside canvas
  Double click the inject node
  In payload field, select string and enter “Hello, “World!

## Slide 53: IoT – Node-RED
Drag and place the debug node inside canvas
Connect the nodes together
In payload field, select string and enter “Hello, “World!
Deploy and Run

## Slide 54
Task #2
Send Message
(from your computer to my computer)

## Slide 55: MQTT

## Slide 56: Send Data through MQTT
MQTT Publisher
MQTT Subscriber
Send ‘Sensor Data’ through MQTT

## Slide 57: Exercise
Sensor at My House
MQTT Publisher
Your Laptop
MQTT Subscriber
Send ‘Data’
Send ‘Data’ through MQTT

## Slide 58: Send & Receive Data using MQTT
MQTT Publisher
MQTT Broker
MQTT Subscriber
Topic
(& Data)
Topic
(& Data)
Send ‘Sensor Data’ through MQTT
Example:
Topic = “xdk10”

## Slide 60: Configure MQTT Broker
Click here
Server: 174.138.28.115
Port: 1883
174.138.28.115

## Slide 61
174.138.28.115:1883

## Slide 62
Task #3 (DIY)
Get data from ESP8266

## Slide 63
Step 1: Use Arduino IDE and upload new code to your (ultrasonic) hardware prototype

## Slide 64: GitHub
Open browser
Type URL
  github.com/ainul21

## Slide 65: GitHub
Open IEEE-STEM-Program

## Slide 66: GitHub
Open Arduino_ESP8266_Code

## Slide 67: Arduino IDE
Task #3
  Go to IEEE-US.ino
  Open file name: IEEE-US.ino
  Copy the code

## Slide 68: Arduino IDE
Paste the code
Click Upload

## Slide 69
Step 2: Import Node-RED flow (from GitHub)

## Slide 70: IoT – Node-RED
Task #3
  Go to NodeRED_Flows

## Slide 71: Node-RED
Task #3
  Open file name: Ultrasonic_Node-red.json
  Copy the code

## Slide 72: Node-RED
Click triple line button
Click Import

## Slide 73: Node-RED
Paste the code
Click Import

## Slide 74
Step 3: Display data from ESP8266 in Node-RED

## Slide 77
Step 3: Display data (from ESP8266) in Node-RED

## Slide 79
Final Mission…

## Slide 80
Can you switch on the light bulb from your computer?

## Slide 81
Let’s try another mission…

## Slide 83: Where is the International Space Station (ISS)?
Exercise: Tracking ISS using Node RED
  Latitude and Longitude
Source Wikipedia: The International Space Station (ISS) is a space station, or a habitable artificial satellite, in low Earth orbit. Its first component launched into orbit in 1998, the last pressurised module was fitted in 2011, and the station is expected to operate until 2028. Development and assembly of the station continues, with components scheduled for launch in 2018 and 2019. The ISS is the largest human-made body in low Earth orbit and can often be seen with the naked eye from Earth.[8][9] The ISS consists of pressurised modules, external trusses, solar arrays, and other components. ISS components have been launched by Russian Proton and Soyuz rockets, and American Space Shuttles.[10]

## Slide 84
http://api.open-notify.org/iss-now.json

## Slide 85: Display on Map?

## Slide 86: IoT – Node-RED
Open browser
Type URL
  github.com/ainul21

## Slide 87: IoT – Node-RED
Open IEEE-STEM-Program

## Slide 88: IoT – Node-RED
Task #2
  Go to NodeRED_Flows

## Slide 89: IoT – Node-RED
Task #2
  Go to TrackISS.json
  Open file name: TrackISS.json
  Copy the code

## Slide 90: IoT – Node-RED
Click triple line button
Click Import

## Slide 91: IoT – Node-RED
Paste the code
Click Import

## Slide 92: IoT – Node-RED
Click Import copy
Import complete

## Slide 93: IoT – Node-RED
Click Deploy
Run the flow by clicking the inject trigger

## Slide 94: IoT – Node-RED
To open the map, copy the URL as below
Open new tab and paste the URL
Add worldmap at the end of /
Press Enter

## Slide 95: IoT – Node-RED
Zoom and drag to achieve the best result of the tracker

## Slide 96: INTRODUCTION TO EMBEDDED SYSTEM
Embedded System

## Slide 97: Similarity?
Embedded system: microprocessor- or microcontroller-based system of hardware and software designed to perform dedicated functions within a larger mechanical or electrical system.

## Slide 98: Embedded System vs. General Purpose
General Purpose Computer | Embedded system
Intended to run a fully general set of applications | Runs a single or limited applications often known at design time
Resources are plenty, Faster is always better | Resources are scarce, operates in fixed run-time constraints, additional performance may not be useful/valuable
Differentiating features: Speed (need not be fully predictable) Cost (eg RM3k vs RM5k per laptop) Software compatibility | Differentiating features: Speed (must be predictable) Power Cost (eg RM2 vs RM2.50) Size Software compatibility problems

## Slide 99
Example of embedded products using microcontroller:

## Slide 100: MICROCONTROLLER, SENSOR & ACTUATOR

## Slide 101
What is microcontrollers ?
Microcontroller is the brain of devices and it operates on its own to control the designed system
A microcontroller is a single chip devices or single chip computers in a small size that it resources are far more limited than those of a desktop personal computer.
It is designed for standalone operation
It is includes:
  Process unit
  RAM & ROM
  I/O
  Buses
  Etc.
e.g., Microcontroller is the robot brain. It allows the designer to interface sensors and specialized control electronics together (along with anything else required for the project) and contain the overall logic of the robot.
Notes: Keyword is standalone

## Slide 102
Microprocessor vs. Microcontrollers
Microprocessor | Microcontroller
It contains fundamental unit of computing –ALU, registers, etc | ROM, RAM, Digital and analog I/O, and peripherals such as communication interfaces are available
Used for tasks that are complex and tricky like development of software’s, games, image processing and other applications with high memory requirement | Single chip and does not require external circuit. Used mostly in embedded system, fast control loop operation.
Fast processing speed | Relatively slower processing speed as compared to microprocessor

## Slide 103: Microprocessor vs. Microcontroller

## Slide 104
Microcontroller Manufacturers

## Slide 105
List down 5 devices around you that contain microcontrollers?

## Slide 106
How to get started?
Simplest development tools
Online community for support and sharing
Cost-effective

## Slide 107
Sensor and Actuator – Interfaced to microcontroller
Physical signals such as temperature, humidity, light, speed, etc. are analog signals (continuous)
Sensors are used to convert the physical signals into digital form that can be used by microcontroller (Input)
Microcontroller will perform the operation according to the program written by users
Appropriate output signal from microcontroller is used to drive actuators of the system (output)
Notes: Analogy with human sense: touch, smell, taste, hearing, sight. Send signal to brain to perceive (tafsir)

## Slide 108
Sensor and Actuator – Interfaced to microcontroller
Solar tracking system
Solar panel will be rotated in such a way that the panel will get ‘maximum’ concentrated sunlight for optimum power generation.
- Sensor : light detector
Actuator : DC or Stepper motor will be rotated according to the calculated angle
Microcontroller : based on the intensity of light, it will calculate the optimum angle for the panel to receive the sunlight

## Slide 109: Check the components given..

## Slide 110: INTRODUCTION TO ARDUINO

## Slide 111
Introduction to Arduino
Arduino is a company/community that designs and manufacture open-source single-board microcontrollers for building digital devices.
Notes: What is Arduino

## Slide 112
Family of Arduino

## Slide 113: Introduction to Arduino: Hardware